## Slide 1
Day 21 — Best Candidate Review: Baseline (Day 18)
Battery SoH estimation using LSTM, GRU and TCN | [Name] | [Date] | Internship / Mentor Review
Setup: sequences_v1.npz (IITG), 2,287 sequences, input 10 steps × 2 features, target SoH. Split 1,516 train / 379 val / 392 test. Day 18: MSE, Adam lr 0.001, batch 32, 30 epochs.
Day 18 baseline — TEST set (392 sequences)
Model | MAE | RMSE | MAPE* | R² | Train time | Inference | Params
LSTM | 0.169238 | 0.215377 | 17.6940 % | −0.944397 | 15.66 s | 0.0511 s | 52,801
GRU | 0.165251 | 0.211757 | 22.030 % | −0.879589 | 21.23 s | 0.0570 s | 40,129
TCN | 0.135121 | 0.184981 | 19.4802 % | −0.434305 | 47.4 s | 0.0896 s | 162,337
* MAPE only on test sequences with SoH ≥ 0.20 (near-zero SoH makes unrestricted MAPE explode). Highlighted = best in column. Model file size: not recorded in any notebook.
What Day 18 showed
TCN: best MAE, RMSE and R²
GRU: smallest model (40,129 params)
LSTM: fastest training / inference
MAPE ranks LSTM < TCN < GRU, differing from MAE/RMSE
Weaknesses that motivated Day 19
R² negative for all three: none beats the mean
Flat-band predictions and early overfitting flagged
Single fixed setup; no systematic tuning
Day 18 verdict: none deployment-ready

## Slide 2
Day 19 — Hyperparameter Tuning & Best Candidates
Grid search per model: 3 × 3 × 3 × 3 = 81 configs × 3 models = 243 total | Selection on VALIDATION RMSE
Search space
Parameter | Range
Units | 32, 64, 128
Learning rate | 0.0001, 0.0005, 0.001
Dropout | 0.0, 0.2, 0.4
Batch size | 16, 32, 64
Early stopping: val_loss, patience 8, max 50 epochs, best weights restored
Test set not used for selection (no test evaluation in notebook)
Best configuration per model — VALIDATION set (379)
Model | Units | LR | Drop | Batch | Epoch | Val RMSE | Val R² | Params
LSTM | 128 | 0.0005 | 0.2 | 32 | 28 | 24.179864 | 0.00002 | 67,201
GRU | 32 | 0.0005 | 0.0 | 32 | 10 | 24.179934 | 0.00001 | 10,881
TCN | 128 | 0.0001 | 0.4 | 32 | 6 | 21.864853 | 0.182 | 251,841
Val MAE: LSTM 15.947 | GRU 15.940 | TCN 14.768
Do not compare with Day 18: validation vs test, apparent 0–100 vs 0–1 scale (inferred, not printed), and Day 19 uses Keras models with different architectures (e.g. single-layer LSTM).
TCN Strongest accuracy candidate: lowest val RMSE, only clearly positive val R²
GRU Lightweight alternative: ~same RMSE as LSTM with 10,881 params
LSTM Baseline / reference candidate: val R² ≈ 0 (near-mean predictions)

## Slide 3
Weaknesses, Week-4 Direction & Mentor Approval
Current best candidate: TCN (accuracy evidence) | Alternative: GRU (efficiency) | Not deployment-ready
Remaining weaknesses (implications are hypotheses)
Observed | Possible implication | Check next
Negative test R² (all models, Day 18) | Not beating mean baseline | Test-evaluate tuned models; mean-predictor baseline
LSTM/GRU val R² ≈ 0; top-10 all ≈ 24.18 | Near-constant predictions | Prediction histograms, learning curves
Flat-band predictions, early overfitting | Limited use of input signal | Predicted vs true SoH plots
MAPE rank ≠ MAE/RMSE rank | Low-SoH sensitivity (SoH ≥ 0.20) | Error by SoH range
TCN largest/slowest; best epoch 6 | Cost vs gain; fast overfit | Seeds, cost comparison
Day 18/19 models differ; no file size, no tuned test results | Evidence not fully linked | Re-run in one setup; record size
Week-4 plan
Test-evaluate tuned models once, consistent scaling
Investigate negative R² and flat-band outputs
Best/worst prediction error analysis
Robustness / ablation study
Record model size and inference time
Finalize model after mentor feedback
Questions for Mentor
Keep TCN as primary candidate?
GRU as lightweight alternative?
Prioritise accuracy or efficiency?
Which robustness/ablation first?
Is current evaluation sufficient?
Missing from files: prediction plots, tuned test metrics, model file size.