## Slide 1: SoH Estimation — Model Development
Objective: compare LSTM, GRU and TCN for battery SoH estimation under the same data split and training setup.
Data & training setup
Train / validation / test split (sequences)
Train
1,516
Val
379
Test
392
Dataset
sequences_v1.npz (IITG)
Samples
2,287 sequences
Input
10 time steps × 2 features
Target
SoH, scaled 0–100 → 0–1
Loss / optimizer
MSELoss · Adam (lr 0.001)
Training
batch 32 · 30 epochs · CPU
Checkpoint
best validation loss
Feature names are not printed in the notebooks.
LSTM
Day 15 · hidden 64 · 2 layers · dropout 0.2
Input
10 × 2
LSTM
2 layers · h=64
Last time
step
FC 64→32
+ ReLU
FC 32→1
(SoH)
GRU
Day 16 · hidden 64 · 2 layers · dropout 0.2
Input
10 × 2
GRU
2 layers · h=64
Last time
step
FC 64→32
+ ReLU
FC 32→1
(SoH)
TCN
Day 17 · kernel 3 · dilations 1, 2, 4 · residual · dropout 0.2
Input
10 × 2
TemporalBlock
×3 (96, 96, 64)
Flatten
64×10 = 640
FC 640→64
ReLU · Drop
FC 64→1
(SoH)
Notes: Slide 1 - What models did I build? The goal of Days 15 to 17 was to estimate battery State of Health with three sequence models: LSTM, GRU and TCN, all trained on the same data. The dataset is sequences_v1.npz with 2,287 sequences, each 10 time steps by 2 features, split into 1,516 train, 379 validation and 392 test sequences. SoH was scaled from 0-100 to 0-1, and every model used MSE loss, Adam at learning rate 0.001, batch size 32, 30 epochs, keeping the checkpoint with the best validation loss. LSTM and GRU are the same design - two recurrent layers with hidden size 64, last time step, then a small fully connected head - while the TCN uses three dilated residual temporal blocks with channels 96, 96, 64, kernel 3 and dilations 1, 2, 4 before flattening into a 640-to-64-to-1 head.

## Slide 2: LSTM vs GRU vs TCN — Performance Comparison
Model | MAE | RMSE | MAPE | R² | Training Time | Inference Time | Parameters / Model Size
LSTM | 0.154379 | 0.198999 | 3522685199974400 %* | −0.659925 | Not recorded | Not recorded | Not recorded†
GRU | 0.143874 | 0.195698 | 815.0989 %* | −0.605318 | Not recorded | Not recorded | 40,129 params
TCN | 0.135121 | 0.184981 | 861.2237 %* | −0.434305 | 47.4 s | Not recorded | 162,337 params
Test set (392 sequences), values as printed in the notebooks. * LSTM MAPE uses sklearn's unclipped formula; GRU and TCN use a denominator clipped at 1e-3, so MAPE is not comparable across rows. † Day 15 prints no parameter count; 52,801 follows from its printed architecture (same arithmetic reproduces GRU 40,129 and TCN 162,337). Model file size is not recorded in any notebook.
Chart: Test MAE and RMSE (lower is better)
| LSTM | GRU | TCN
MAE | 0.15438 | 0.14387 | 0.13512
RMSE | 0.199 | 0.1957 | 0.18498
Key findings
TCN is best on every error metric: MAE 0.135121, RMSE 0.184981, R² −0.434305.
Ranking is TCN < GRU < LSTM on both MAE and RMSE (lower is better).
R² is negative for all three models — none beats predicting the mean on the test set.
GRU is the smallest recorded model (40,129 params); TCN has 162,337, about 4× GRU.
MAPE cannot rank the models: SoH targets include 0.0.
Notes: Slide 2 - How did they perform? This is the single comparison table from the three notebooks, all on the same 392-sequence test set. TCN is best on MAE, RMSE and R-squared, with MAE 0.135, followed by GRU at 0.144 and LSTM at 0.154, but the gaps are small. The important honest point is that R-squared is negative for all three, so none of them beats simply predicting the mean SoH yet. On cost, GRU has 40,129 parameters and TCN has 162,337, roughly four times larger; only the TCN training time of 47.4 seconds was recorded, and inference time and model file size were not recorded for any model. MAPE is shown but I would not use it for ranking, because the SoH targets include zero values and the LSTM notebook used a different MAPE formula from the GRU and TCN notebooks.

## Slide 3: Model Comparison & Next Steps
1
OBSERVATIONS
2
LIMITATIONS
3
SHORTLIST / NEXT EXPERIMENT
Best: TCN. MAE 0.135121, RMSE 0.184981, R² −0.434305.
Lightest: GRU, 40,129 params (LSTM 52,801†, TCN 162,337).
Different designs: LSTM and GRU read the last time step; TCN uses dilated residual convolutions over all 10 steps.
Gaps are small: TCN beats GRU by 0.0088 MAE and LSTM by 0.0193.
† derived from the printed architecture
R² negative for all three (−0.434 to −0.660).
Early overfitting: LSTM and GRU best val loss at epoch 2, ~0.088 by epoch 30; TCN val loss swings 0.053–0.083.
Failure pattern: predictions sit in flat bands (~0.5–0.55, ~0.65–0.72) while actual SoH varies; SoH ≈ 0 predicted ≈ 0.5.
MAPE unreliable: targets include SoH = 0; LSTM 3.5×10¹⁵ %, GRU/TCN >800 %.
Small input: 2 features, sequence length 10, 1,516 train sequences; one run each.
Missing: inference time and model size for all; training time for LSTM and GRU.
BEST PREDICTIVE PERFORMANCE
TCN
Lowest MAE / RMSE, highest R² (still negative).
LIGHTWEIGHT / EFFICIENT
GRU
40,129 params; beats LSTM on MAE, RMSE, R².
Next: take TCN and GRU into deeper experiments — record timing and model size, use one MAPE definition, and diagnose the flat-band predictions and early overfitting.
Notes: Slide 3 - What did I learn and what next? TCN is the best predictor of the three, and GRU is the lightest recorded model, with 40,129 parameters; LSTM is the weakest on error and R-squared, so I keep it only as a baseline. The main limitation is that every R-squared is negative, and the loss curves show LSTM and GRU reach their best validation loss at epoch 2 and then get worse, while TCN's validation loss swings between 0.053 and 0.083. In the predicted-versus-actual plots all three models place predictions in a few flat bands instead of following actual SoH, and sequences with SoH near zero are predicted near 0.5. We also have only 2 input features, a sequence length of 10, one run per model, and no inference-time or model-size measurements. Next I would carry TCN and GRU into deeper experiments, starting by fixing the evaluation - one MAPE definition, timing and model size recorded - and then diagnosing the flat-band behaviour and early overfitting.